## Slide 1: SMART PARKING

## Slide 2: Components
Microcontroller- Raspberry Pi
Sensor – ultrasonic sensor
Rasberry Pi:
The Raspberry Pi is a popular, low-cost, single-board computer that is used for a wide range of computing projects. It was developed by the Raspberry Pi Foundation and has gained immense popularity due to its affordability, versatility, and a large community of users and developers.

## Slide 3
Ultrasonic sensor:
An ultrasonic sensor is a device that uses ultrasonic sound waves to measure distances to objects or to detect their presence. These sensors are commonly used in various applications, including robotics, industrial automation, and IoT.

## Slide 4: Coding
Import Rpi.GPIO as GPIO import time # Define GPIO pins for the ultrasonic sensor trigger_pin = 23 # GPIO23 (or any other available GPIO pin) echo_pin = 24 # GPIO24 (or any other available GPIO pin) # Set GPIO mode and configure pins GPIO.setmode(GPIO.BCM) GPIO.setup(trigger_pin, GPIO.OUT) GPIO.setup(echo_pin, GPIO.IN)
# Function to measure distance using the ultrasonic sensor def measure_distance(): # Send a short pulse to trigger the sensor GPIO.output(trigger_pin, GPIO.HIGH) time.sleep(0.00001) GPIO.output(trigger_pin, GPIO.LOW) # Measure the duration of the echo pulse while GPIO.input(echo_pin) == 0: pulse_start_time = time.time() while GPIO.input(echo_pin) == 1: pulse_end_time = time.time() # Calculate the distance based on the speed of sound (34300 cm/s) pulse_duration = pulse_end_time – pulse_start_time distance = (pulse_duration * 34300) / 2 # Divide by 2 for one-way distance return distance try: while True: # Measure the distance dist = measure_distance() print(“Distance: {:.2f} cm”.format(dist)) # Check parking space status based on the distance if dist < 20: # Adjust the threshold as needed print(“Parking space is occupied.”) else: print(“Parking space is vacant.”) time.sleep(1) # You can adjust the sleep interval for how often to check the status except KeyboardInterrupt: GPIO.cleanup()

## Slide 5: Output
Distance: 15.32 cm Parking space is occupied. Distance: 21.46 cm Parking space is vacant. Distance: 17.85 cm Parking space is occupied. …